## Slide 1: DWA*code

## Slide 2: Struct
struct OBS { //Express obstacles
double x;
double y;
double r;
};
struct VEL { //Express velocity
double v;
double w;
double unsafety;//0~1
int i; //Corresponding ITV index, easy for indexing
bool safe;//If it can stop before collision
bool reach;//If it can be reached immediately
int hi;//position in the VEL array
int wi;
};

## Slide 3: ObsArray
A data type for saving all obstacles.
Example code
vector <double> range; // polar-type laser data
vector <double> rad; //polar-type laser data
ObsArray obsarr;
obsarr.set_obs_laser_array(range,rad); // Transform the polar data into OBS struct, it will be saved in obsarr.obs, a vector<OBS> type array.

## Slide 4: VelItv
Compute the minimum colliding distance of a velocity (v,w)
VelItv(double ang_resolution,double dist_max);//(degree, meter)
  ang_resolution: angle resolution in velocity space, 180/(ang_resolution) + 1 trajectories are computed.
  dist_max: collision_free distance
void SetITV_Multi(vector<OBS>& obsarr);
  Compute the collision distane give a obstacle array.
Example code
ObsArray obsarr;
VelItv vitv(1,80); //initialize
obsarr.set_obs_laser_array(range,rad);
vitv.SetITV_Multi(obsarr.obs); //computing

## Slide 5: DWA
Find admissible velocities from obstacle configurations.
DWA(double* limits,RobotTra::VelItv& velitv);
  double limits[9] is a array, contains parameters of DWA.
  Limits[0] = Maximum forward velocity (m/s)
  Limits[1] = Minimum forward velocity (m/s)
  Limits[2] = Maximum rotating velocity (rad/s)
  Limits[3] = Minimum rotating velocity (rad/s)
  Limits[4] = Maximum forward acceleration (m/s^2)
  Limits[5] = Maximum rotating acceleration (rad/s^2)
  Limits[6] = search resolution of forward velocity (m/s)
  Limits[7] = search resolution of rotating velocity (rad/s)
  Limits[8] = sampling time (s)
  That is, the DWA object will have a 2-D velocity array of height == (limit[0] – limit[1])/limit[6], width == (limit[2] – limit[3])/limit[7].

## Slide 6: DWA
Example code
double vlim[] = {0.5,0,1,-1,0.5,1,0.1,0.1,0.5};
ObsArray obsarr;
VelItv vitv(1,80); //initialize
DWA dwa(vlim,vitv);
obsarr.set_obs_laser_array(range,rad); //Set sensor information
dwa->Update_Vel_State(obsarr,bestnode.v,bestnode.w); //Computing
vector<VEL> &cands = dwa->candidates; //dwa->GetCandidates();

## Slide 7: TraTree
Trajectory tree.
Use to implement look-ahead controller.
Process:
  1. Find the best node from trajectory tree.
  2. Compute DWA from the best node, push new nodes into the tree.
  3. back to step 1, until the goal is reached.
Important member function
  void TraSearch(vector<OBS>& initobs,double& rv,double& rw, double lgx,double lgy,int MaximumNodes); //
  rv,rw: present robot velocity, the solution will then be saved in them.
  lgx,lgy: goal location.
  Maximumnodes: The above process will be executed for MaximumNodes times.

## Slide 8: TraTree
Example code
double vlim[] = {0.5,0,1,-1,0.5,1,0.1,0.1,0.5};
ObsArray obsarr;
VelItv vitv(1,80); //initialize
DWA dwa(vlim,vitv);
obsarr.set_obs_laser_array(range,rad); //Set sensor information
DWAtree.dwa = this->dwa; //Initialization
DWAtree.TraSearch(obsarr.obs, v, w, 20, 0, 200); //Computing